## Slide 1
INITIAL FIRE ENGINEER
PUMP OPERATIONS
Truck checks · Driving with due regard · Hydrants · Apparatus placement · Pump engagement
CAPSTONE 2 | NFPA 1002 | FIRE & EMS INSTRUCTOR I AND II
April 28, 2026 · 45-Minute Presentation
Student Roster

## Slide 2
LEARNING OBJECTIVES
Describe the responsibilities of the apparatus driver/operator under NFPA 1002
Perform a daily/shift apparatus check and document deficiencies
Operate a fire apparatus with due regard, applying ORC 4511.03 / 4511.041
Identify hydrant types (Storz vs threaded) and execute a forward and reverse lay
Position the apparatus to maximize crew safety, scene access, and water supply
Engage the pump, set pressure, and supply attack lines from tank or hydrant
Carry out the secondary duties of the engineer while serving as command's situational eyes
NFPA 1002 | Mileage Design

## Slide 3
LEARNER CHARACTERISTICS
NFPA 1002 — Target Audience
Active firefighters preparing for the driver/operator position
Hold valid Firefighter I or I&II certification under OAC 4765-18
Adult learners with field experience on engine companies
Familiar with hose loads, basic apparatus layout, and SCBA use
Variable experience with apparatus driving and pump panel operation
Motivated to qualify as engineer and assume the responsibility of the wheel and panel
NFPA 1002 | Mileage Design

## Slide 4
THE ENGINEER'S ROLE — NFPA 1002
NFPA 1002 is the standard for Fire Apparatus Driver/Operator Professional Qualifications
The DO is responsible for the safe transport, positioning, and pump operation of the rig
On the rig before the call — and stays with it until back in quarters, ready for the next response
Two NFPA 1002 chapters frame the position:
  Chapter 4 — General Requirements: inspection, maintenance, driving, backing, defensive driving
  Chapter 5 — Pump Operations: tank, hydrant, drafting, relay, pressure management
Judged less on speed and more on consistency — the rig that doesn't crash and the line that doesn't lose pressure
NFPA 1002 | Mileage Design

## Slide 5
DAILY APPARATUS CHECK
Conducted at shift change — signed off in the apparatus log
Walk-around (clockwise from driver door):
  Body damage, mirrors, lights (low/high beam, brake, turn, scene, warning)
  Tires — tread depth, sidewall, lug nut indicators, valve caps, air pressure
  Compartments — latched, inventoried, equipment secured
Engine bay — oil, coolant, power steering, washer fluid, belts, hoses
Cab — SCBA seats charged, MDT/radio responsive, emergency lighting cycle test
Pump panel — primer cycle, tank-to-pump, gate valves, intake/discharge caps, water level
Air system — build to governor, leak-down test, low-air warning
Document deficiencies on the OOS log; notify officer if anything is safety-critical
NFPA 1002 | Mileage Design

## Slide 6
CREW RESPONSIBILITIES BEFORE ROLLING
CREW ROLES
Officer — confirms address, radio, tactical worksheet
FF1 (Backstep R) — attack line, irons, primary search
FF2 (Backstep L) — hydrant, water supply, backup line
DO — best route, apparatus position, pump readiness
All — seatbelts before wheels move (non-negotiable)
COMMON PRE-ROLL FAILURES
Address not confirmed; rig rolls toward wrong street
SCBA not donned enroute — delays entry on arrival
Accountability tags forgotten
Cab doors not latched — warning chime ignored
Hose load disturbed from previous call
NFPA 1002 | Mileage Design

## Slide 7
DRIVING WITH DUE REGARD
Due regard — the legal duty to operate an emergency vehicle with the safety of all persons in mind, regardless of right-of-way granted by warning lights
Ohio Revised Code references:
  ORC 4511.03 — Emergency vehicles must come to a complete stop before proceeding through any red signal or stop sign
  ORC 4511.041 — Driver of an emergency vehicle is not relieved from the duty to operate with due regard for the safety of all persons
Code 3 — lights and siren; Code 1 — normal traffic flow, no warning devices
Intersections: stop, scan all four directions, eye contact with civilians, proceed lane-by-lane
Backing — never alone; spotter at left rear, two taps to stop, mirror sweeps every 5 seconds
Use engine retarder/Jake brake on grades; ride the throttle, not the service brakes
Reduce speed to 60% of posted limit on curves; full water tank shifts the center of gravity
NFPA 1002 | Mileage Design

## Slide 8
COMMUNICATION & RADIO AWARENESS
Enroute — monitor dispatch and primary tactical channel; acknowledge updates
On arrival — officer gives size-up; the DO listens for the water-supply call
Mark your hydrant: "Engine 12 has a hydrant at Main and 5th, forward laying 200 feet of 5-inch."
Switch to the assigned tactical or fireground channel as directed
If command requests a water-supply update, give a number: PSI, GPM, or tank water remaining
If you hear MAYDAY — stop non-essential traffic, dedicate a discharge to the RIT line, report readiness
NFPA 1002 | Mileage Design

## Slide 9
HYDRANT TYPES — STORZ VS THREADED
STORZ (5" LDH)
Sexless quarter-turn coupling — no male/female threads
Connect, rotate 1/4 turn clockwise, lock pin engages
Faster connection, less likely to cross-thread
Standard for forward-lay supply on modern apparatus
Open hydrant slowly to charge; full open after charged
THREADED (NST/NH)
National Standard Thread — 4.5" steamer + two 2.5" outlets
Use hydrant wrench to remove cap and open valve
Hand-tight first — avoid cross-threading; finish with wrench
Common in older systems; carry Storz-to-NST adapters
"Down to charge, up to shut" — rotation reminder
NFPA 1002 | Mileage Design

## Slide 10
FORWARD LAY VS REVERSE LAY
Forward lay — engine drops at hydrant (FF2 jumps off), then drives to fire laying supply line behind it
  Engine arrives at scene fully positioned for attack
  Best when hydrant is between dispatch route and the fire
Reverse lay — engine arrives at fire, drops attack lines, then drives back to hydrant laying supply line
  Useful when hydrant is past the fire, or when a second engine establishes supply
  Pump operator at the hydrant; another driver pumps the attack engine
Department SOP usually defines the default lay; deviation requires officer approval
NFPA 1002 | Mileage Design

## Slide 11
APPARATUS PLACEMENT
The first piece sets the geometry of the entire scene
Position past the structure (~25 ft) so the front clears the building — gives truck company room to set up
Stay out of the collapse zone — minimum 1.5x building height for unstable structures
Check overhead — power lines, tree limbs, awnings; aerial apparatus needs vertical clearance
Egress — never block your own retreat; second engine should pass on at least one side
Wheels chocked, brake set, transmission in pump gear (or neutral with parking brake per manufacturer)
Highway incidents — block one lane wider than work area, wheels turned away from crew, scene lights toward oncoming traffic
NFPA 1002 | Mileage Design

## Slide 12
PUMP ENGAGEMENT & PRESSURE MANAGEMENT
Sequence (typical midship pump):
  Truck stopped, parking brake set
  Transmission to NEUTRAL
  Pump shift switch to PUMP — wait for green "OK to pump" indicator
  Transmission to DRIVE — rear wheels stay still, pump turns
  Open tank-to-pump valve; pump now pressurized from booster tank
Charge attack line to target pressure (1.75" handline at 100 PSI nozzle + friction loss)
Transition to hydrant: open intake gate slowly, close tank fill, monitor compound gauge
Use PRESSURE GOVERNOR mode (PSI) for handlines; RPM mode only for relay or master stream per SOP
Watch the gauges, not the fire — that's the FF1's job
NFPA 1002 | Mileage Design

## Slide 13
GENERATOR, LIGHTING & SECONDARY DUTIES
Once water is flowing and pressure is stable, the engineer rotates to secondary duties:
  Scene lighting — deploy generator, raise the light tower, position cord reels for interior crew
  Ladders — throw a ground ladder to a second-floor window for the search team's bailout
  Tools — stage irons, pike poles, K-12 saw, thermal imager at the front step
  SCBA bottles — pull spare bottles from the compartment, stage them at rehab
  Hydration — water bottles to crews coming off air; rehab area set up
  Salt / shovel — ice control around the rig and hose bed in winter
  Backup hose lines — pull a second 1.75" to the front door before it's needed
Every minute spent setting up secondaries early saves three minutes when command asks for them
NFPA 1002 | Mileage Design

## Slide 14
PUMP OPERATOR AS COMMAND'S EYES
The DO has the only continuous 360° view of the building once interior crews go inside
Report changes to command:
  Smoke conditions changing color, volume, velocity, density (the four attributes of fire behavior)
  Fire showing in new openings
  Structural movement — sagging eaves, spalling brick, settling porch
  Civilian arrival or self-evacuation
  Approaching apparatus or police, blocked egress, downed power lines
Water supply forecasting — if your tank is at 25% and you're not on a hydrant yet, that's a command notification, not a panic
RIT-line readiness — one discharge gated and pre-charged for MAYDAY response
NFPA 1002 | Mileage Design

## Slide 15
SUMMARY & KEY TAKEAWAYS
The engineer owns the rig, the pump, and the situational view of the scene
Daily apparatus check is the most important task of the shift — every shift
Drive with due regard — the law and the math both say slow down at intersections
Forward lay vs reverse lay — know your SOP, mark the hydrant on radio
Pump engagement is a sequence — Park → Neutral → Pump → Drive → Tank-to-pump
Secondary duties save lives — set them up before they're needed
Be command's eyes — report fire behavior, structural changes, water-supply status
NFPA 1002 | Mileage Design

## Slide 16
QUIZ TIME
10 QUESTIONS
Multiple choice · Discuss as a class
Take it on your phone — scan the QR or visit the page
bbishilany.github.io/nicks-capstone/capstone-2.html#quiz
NFPA 1002 | Mileage Design

## Slide 17
QUESTION 1 OF 10
Which NFPA standard governs Fire Apparatus Driver/Operator Professional Qualifications?
A
NFPA 1001
B
NFPA 1041
C
NFPA 1002
D
NFPA 1500
ANSWER: C) NFPA 1002
NFPA 1002 | Mileage Design

## Slide 18
QUESTION 2 OF 10
"Due regard" means the emergency vehicle driver must:
A
Always have right of way under lights and siren
B
Operate with the safety of all persons in mind regardless of warning devices
C
Drive at any speed necessary to reach the call
D
Never stop at red lights when responding
ANSWER: B) Operate with the safety of all persons in mind regardless of warning devices
NFPA 1002 | Mileage Design

## Slide 19
QUESTION 3 OF 10
A Storz coupling connects to a hydrant by:
A
A quarter turn clockwise — sexless coupling, no threads
B
Five full clockwise turns with a hydrant wrench
C
Threading the male end into the female outlet
D
A friction-fit clamp tightened with a strap wrench
ANSWER: A) A quarter turn clockwise — sexless coupling, no threads
NFPA 1002 | Mileage Design

## Slide 20
QUESTION 4 OF 10
In a forward lay, the engine:
A
Drops a firefighter at the hydrant, then drives to the fire laying supply line behind it
B
Arrives at the fire first, then drives back to the hydrant
C
Pumps from tank water only, never connecting to a hydrant
D
Stages two blocks away and waits for command
ANSWER: A) Drops a firefighter at the hydrant, then drives to the fire laying supply line behind it
NFPA 1002 | Mileage Design

## Slide 21
QUESTION 5 OF 10
A typical 1.75" handline is supplied at what nozzle pressure (smooth-bore not used)?
A
50 PSI
B
75 PSI
C
100 PSI
D
150 PSI
ANSWER: C) 100 PSI
NFPA 1002 | Mileage Design

## Slide 22
QUESTION 6 OF 10
When backing the apparatus, the spotter should be positioned:
A
At the front bumper
B
At the left rear of the apparatus, in the driver's mirror sight line
C
Inside the cab giving verbal directions
D
Wherever convenient — backing alone is acceptable in an empty bay
ANSWER: B) At the left rear of the apparatus, in the driver's mirror sight line
NFPA 1002 | Mileage Design

## Slide 23
QUESTION 7 OF 10
The correct sequence for engaging a midship pump is:
A
Drive → Pump shift → Park brake → Tank-to-pump
B
Pump shift → Drive → Park brake → Tank-to-pump
C
Park brake → Neutral → Pump shift → Drive → Tank-to-pump
D
Tank-to-pump → Pump shift → Drive → Park brake
ANSWER: C) Park brake → Neutral → Pump shift → Drive → Tank-to-pump
NFPA 1002 | Mileage Design

## Slide 24
QUESTION 8 OF 10
When positioning the engine at a residential structure fire, you should:
A
Stop directly in front of the door for shortest hose stretch
B
Park on the lawn for stability
C
Pull into the driveway and block the truck company
D
Pull approximately 25 feet past the structure to leave room for the truck company
ANSWER: D) Pull approximately 25 feet past the structure to leave room for the truck company
NFPA 1002 | Mileage Design

## Slide 25
QUESTION 9 OF 10
Which of the following is NOT a typical secondary duty of the engineer once water is flowing?
A
Throwing ground ladders for crew bailout
B
Conducting interior primary search
C
Staging spare SCBA bottles at rehab
D
Pulling a backup 1.75" line to the front door
ANSWER: B) Conducting interior primary search
NFPA 1002 | Mileage Design

## Slide 26
QUESTION 10 OF 10
The four attributes of fire behavior the pump operator should report to command are:
A
Heat, light, smoke, sound
B
Color, smell, texture, temperature
C
Volume, velocity, density, color
D
Speed, height, angle, distance
ANSWER: C) Volume, velocity, density, color
NFPA 1002 | Mileage Design

## Slide 27
REFERENCES
NFPA 1002: Standard for Fire Apparatus Driver/Operator Professional Qualifications (2024)
NFPA 1901: Standard for Automotive Fire Apparatus (2022)
ORC 4511.03 — Emergency Vehicles at Red Signals
ORC 4511.041 — Due Regard for Safety
U.S. Fire Administration. Emergency Vehicle Safe Operations for Volunteer and Small Combination Fire Departments (2017)
IFSTA. Pumping Apparatus Driver/Operator Handbook (4th ed., 2022)
Ohio Division of EMS. Firefighter I & II Course Packet
NIOSH Fire Fighter Fatality Investigation and Prevention Program
NFPA 1002 | Mileage Design

## Slide 28
QUESTIONS?
Thank you for your attention.
Capstone 2 · Initial Fire Engineer / Pump Operations · NFPA 1002
bbishilany.github.io/nicks-capstone
NFPA 1002 | Mileage Design